## Slide 1: ECE 477 MIDTERM DESIGN REVIEW
Team 16 : Track-On-Track

## Slide 2: OUTLINE
Project Overview
Major Components
Block Diagram
Packaging Design
Electrical Schematic
PCB Layout
Prototyping Progress
Software Development Status
Project Timeline
Questions

## Slide 3: PROJECT OVERVIEW
Device which is able to find its own location using assisted GPS from an onboard cell modem.
Device can also use Bluetooth which can be used to approximate distance based on strength of signal.
Device is designed to fit into backpack or luggage and transmit its location to user’s smartphone through SMS messages, and can communicate at close range using Bluetooth.
Once smartphone receives GPS coordinates, it will plot those onto a Google Maps display to show user exact location of their belongings.

## Slide 4: PSSCS
An ability to communicate with the user through Bluetooth in short distances.
An ability to communicate with the user through a cell modem over SMS in long distances.
An ability to display operating mode, battery life, and cell signal through an LCD.
An ability to detect the devices location.
An ability to control the device through a smartphone application.

## Slide 5: MAJOR COMPONENTS: Microcontroller
MSP430FR6989 selected as microcontroller for project
128 kB FRAM, 2 kB RAM, .375 mA @ 1 MHz, 2 UART, 4 SPI, 83 pins.
Chosen because it is very power efficient while still having enough memory and speed to perform required processes

## Slide 6: MAJOR COMPONENTS: Cell Modem
SIM5320A selected as GSM modem for our project
Supports 2G and 3G connections
Adafruit breakout board available
Built in support for variety of protocols including SMS, MMS, HTTP, FTP, SSL, DNS
Chosen because of flexibility of the component along with example code and board

## Slide 7: MAJOR COMPONENTS: Bluetooth
RN4020 chosen as bluetooth module for project
7 dBm, <900 nA while asleep, 16 mA while operating, support SPI and UART, 1 Mb/s transmission
Chosen due to balance between power consumption and transmission power, under optimal conditions, can transmit 100 meters

## Slide 8: MAJOR COMPONENTS: Display
EA DOGS104W-A chosen as LCD display for our project
Low power consumption (440 µA typical)
Backlight optional
4 lines with adjustable character sets
SPI or I2C interface for simplicity with our microcontroller

## Slide 9: MAJOR COMPONENTS: Battery
PRT-13856 chosen as rechargeable battery for project
3.7 V, 6 Ah, < 150 g, 51 * 73 * 20 mm
Provides enough voltage to run all components
Under minimal use conditions, will power device for approximately 51 days
Weight and size wise, battery is small enough to not impact design considerably

## Slide 10: BLOCK DIAGRAM

## Slide 11: PACKAGING DESIGN
A small box that has openings for LCD, three push buttons, micro USB port, and a switch

## Slide 12: ELECTRICAL SCHEMATIC

## Slide 13: PCB LAYOUT OVERVIEW: Top Layer

## Slide 14: PCB LAYOUT OVERVIEW: Bottom Layer

## Slide 15: PCB LAYOUT: Bluetooth Module
Decoupling Capacitor
Antenna out of board

## Slide 16: PCB LAYOUT: JTAG and Reset
Unused JTAG pins connected to cell modem UART pins for debugging

## Slide 17: PCB LAYOUT: Microcontroller
Decoupling capacitors placed underneath
No external oscillator needed

## Slide 18: PCB LAYOUT: Cell Modem and SIM
SIM card slot placed under the cell modem
Antenna SMA interface out of board
Antenna U.FL interface placed on another side
Decoupling capacitors

## Slide 19: PCB LAYOUT: Power Block
MicroUSB for power input
JST header for battery
On edge of board
Trace width of 32 mils
3 status LEDs

## Slide 20: PCB LAYOUT: LCD & Buttons
LCD placed on board for stability
6x6mm pushbuttons to interact with device
Close to edge of board

## Slide 21: SOFTWARE DEVELOPMENT PROGRESS
Embedded Software
  Send and receive SMS messages from app
  Communicate with Bluetooth with app
  Respond to commands from device
Smartphone App
  Send and receive SMS messages from device
  Communicate with Bluetooth with device
  Display location of device on Google Maps
  Display relative distance based on Bluetooth
Complete
Partially Complete
Incomplete

## Slide 22: SOFTWARE DEVELOPMENT PROGRESS
Embedded Software
Ability to receive SMS messages
Respond to physical buttons
Ability to send SMS messages
Communicate using Bluetooth
Use speaker and LCD when requested
Read and respond to Bluetooth commands
Send requests for coordinates
Organize and send info to app
Read and respond to commands
Receive and translate coordinates

## Slide 23: SOFTWARE DEVELOPMENT PROGRESS
Smartphone App
Ability to receive SMS messages
Ability to send SMS commands
Communicate using Bluetooth
Display signal strength of Bluetooth
Send commands using Bluetooth
Tailor messages via options menu
Display location on Google Maps

## Slide 24: PROJECT TIMELINE
Week 8: Get feedback for PCB, incorporate into design
Week 9: Finish and submit PCB, smartphone app functional for testing
Week 10: Spring Break
Week 11: Receive PCB, solder board, test embedded program
Week 12: Finish main portions of embedded program, begin testing of main features
Week 13: Test full design for vital aspects such as SMS coms and GPS coordinates
Week 14: Finish packaging, finish app, finish embedded soft., test other features
Week 15: Finish all features, test edge cases, find limits of device
Week 16: Design Showcase

## Slide 25: QUESTIONS?